## Slide 1: Harnessing Marvell Accelerators with Open vSwitch(OVS) Hardware Offload for Accelerated Network Performance 20-21st November 2024 Harman Kalra – Senior Principal Engineer Jerin Jacob – Senior Director

## Slide 2
netdev-dpdk
Hardware offload boosts packet processing speed by using specialized hardware, enhancing throughput and minimizing latency
Reduced Host CPU Load: Offloading tasks to the NIC frees up CPU cycles, allowing the host system to handle other critical tasks efficiently
Control stack for dedicated switching hardware
VF Representors represent VFs in OVS, facilitating management and monitoring of network traffic
OVS handles exception packets by classifying them and offloading the flow to dedicated hardware
Subsequent packets match the offloaded flow and take the appropriate actions
Flow Classifier/Embedded Switch
No Kernel Space Role
VM1
dpif-netdev (User space forwarding)
OvS-vSwitchd
Uplink
RTE Flow
RX/TX Burst
VF representors PMD
RTE Flow
RX/TX Burst
PF PMD
PF
VF1
VFn
VF Driver
VM1
VF Driver
VM1
VF Driver
Overview – Open vSwitch (OVS) Hardware Offloading
VM – Virtual Machine
PF- Physical Function
VF – Virtual Function
VF Rep – Virtual Function Representor

## Slide 3: Introduction to Marvell Octeon CN10K DPU

## Slide 4: Marvell Octeon CN10K DPU
8 to 24 64-bit ARM Neoverse N2 cores with speeds up to 2.7 GHz
Up to 1 MB L2 per core and total 48 MB LLC cache
Up to 6 DDR5 at 5600 MTS
Integrated 1Terabit switch
Comprehensive hardware accelerators
  Hardware ML/AI Acceleration Engine
  True inline crypto
  Highly programmable packet processors
  PCIe DMA Acceleration
Rich set of I/O
  PCIe 5.0
  Up to 16 x50G ethernet lanes
  MACsec support
  Up to 56G SerDes lanes

## Slide 5: CN10K - Packet Walkthrough – Hardware View
IPsec-Rx
IPsec-Tx
Logical MACs 100G,
50G,
40G,
10G,
1G,
PCIe – SDP (System DPI packet interface Unit)
Loopback
Network Pool Allocator
(NPA)
ARM Neoverse N2 Cores
Schedule/
Synchronize/Order Unit
(SSO)
Add packets to CQ ring
Get work
NPA Buffer
Allocation
Free buffer
to NPA
Pull packets from CQ ring
Inline
IPsec - RX
Add work
Enqueue packets to SQ for Transmit
Outbound IPsec-TX
Encrypt
SQ0
NIX-Tx
SQ1
SQn
Network Interface Controller Unit
Schedulers + Shapers
Software buffer alloc/free
Timer Unit (TIM)
Crypto
(CPT)
Compress
(ZIP)
Regex (REE)
Lookaside engines
NIX CQ
ARM N2
ARM N2
ARM N2
AES
SVE2
FPU
VGIC
SMMU
64K I cache
1MB L2
64K D cache
RSS
RQ0
NIX-Rx
RQ1
RQn
Network Interface Controller Unit
Add work
Vector add work
RX
TX
Plain
Plain
Encrypt
DMA Unit (DPI)
ML/AI Accelerator
CPT
Plain packet post-decryption
Packet Parser
Key Generation
Network Parser and CAM Unit
MCAM
NPC-Rx
Packet Parser
Key Generation
NPC-Tx
MCAM
Network Parser and CAM Unit
Cryptographic Accelerator Unit
Hardware enqueue/dequeue operation

## Slide 6: CN10K - Packet Walkthrough – Software View
Ethdev Ports
Ethernet MAC
PCIe Host
Loopback
Network Pool Allocator
(NPA)
ARM Neoverse N2 Cores
rte_eth_rx_burst()
rte_event_enqueue_burst()
rte_security_set_pkt_metadata()
Encrypt
Packet Parser
Key Generation
MCAM
rte_flow
rte_mempool_alloc/free()
Packet Parser
Key Generation
rte_flow
NPC-Tx
MCAM
ARM N2
ARM N2
ARM N2
AES
SVE2
FPU
VGIC
SMMU
64K I cache
1MB L2
64K D cache
RSS
RQ0
RQ1
RQn
rte_ethdev, rte_mtr
RX
TX
Plain
Plain
Encrypt
rte_mempool
rte_eth_tx_burst()
rte_event_dequeue_burst()
rte_eth_rx_queue_setup()
rte_eth_tx_queue_setup()
EAL
Mbuf
Hash, LPM,ACL
(De)Fragmentation
SW Libraries
Ring
Pdump
Supports both Poll mode and event mode by enabling/disabling scheduler
MKEX/KPU Profile
rte_mempool_create/destroy()
rte_event_dev_configure()/
rte_event_queue_setup()
rte_security_session_create()
E.g. Lookaside crypto
rte_cryptodev_en(de)queue_burst()
rte_eth_tx_burst()
HW Scheduler
(SSO)
rte_eventdev
Timer (TIM)
Crypto (CPT)
Compress (ZIP)
Regex (REE)
DMA (DPI)
rte_event_timer_adapter
rte_cryptodev
rte_compress
rte_regexdev
rte_event_dma_adapter
ML/AI
Lookaside engines
rte_mldev
NIX CQ
IPsec-Rx
IPsec-Tx
CPT
Cryptographic Accelerator Unit
Network Parser and CAM Unit
Network Interface Controller Unit
SQ0
rte_ethdev, rte_tm
SQ1
SQn
Network Interface Controller Unit
Schedulers + Shapers

## Slide 7
DPDK Subsystem/Library | Abstracted Hardware Controllers/ Accelerators | High-Level Description of APIs
rte_ethdev, rte_event_eth_[rt]x_adapter, | NIX (RPM, SDP, LBK) | Configure the network controller. Set up its RX and TX queues. Start the controller
 |  | Send and Receive packets in poll mode.
 |  | See https://doc.dpdk.org/api/rte__ethdev_8h.html for more information
rte_mempool | NPA | Memory allocation APIs
 |  | See https://doc.dpdk.org/api/rte__mempool_8h.html for more information
rte_flow | NPC | Flow-classification library, program packet-matching and associated actions in hardware through-flow rules.
 |  | See https://doc.dpdk.org/api/rte__flow__classify_8h.html for more information
rte_tm | NIX | Traffic Manager API: Hierarchical scheduling, traffic shaping, congestion-management, packet marking.
 |  | See https://doc.dpdk.org/api/rte__tm_8h.html for more information
rte_cryptodev, rte_event_crypto_adapter | CPT | APIs for provisioning cipher and authentication operations.
 |  | See https://doc.dpdk.org/api/rte__cryptodev_8h.html for more information
rte_security | CPT | A framework for managing and provisioning of security protocol operations offloaded to hardware e.g. IPSEC.
 |  | See https://doc.dpdk.org/api/rte__security_8h.html more information
DPDK (Data Plane Development Kit) subsystem mapping

## Slide 8
DPDK Subsystem/Library | Abstracted Hardware Controllers/ Accelerators | High-Level Description of APIs
rte_eventdev | SSO | Support for event-driven programming model; offers applications, automatic multicore scaling, dynamic load-balancing, pipelining, packet ingress order, maintenance and synchronization services to simplify application packet-processing.
 |  | See https://doc.dpdk.org/api/rte__eventdev_8h.html for more information
rte_event_timer_adapter | TIM | Part of the event driver programming model, the timer adapter provides periodic events that can be used in cases like TCP timers.
 |  | See https://doc.dpdk.org/api/rte__event__timer__adapter_8h.html for more information
rte_dmadev, rte_event_dma_adapter | DPI | API allows applications to configure and use generic devices that have no specific type available in the DPDK.I In OCTEON TX2 it can be used for the DMA controller ( DPI).
 |  | See https://doc.dpdk.org/api/rte__dmadev_8h.html for more information
rte_regexdev | REE | Regular Expression (RegEx) Device Library provides a RegEx device framework for management and provisioning of hardware and software.
 |  | See https://doc.dpdk.org/api/rte__regexdev_8h_source.html for more information
rte_mldev | ML | Machine Learning (ML) Device Library provides a Machine Learning device framework which support a number of ML operations including device handling and inference processing.
 |  | See https://doc.dpdk.org/api/rte__mldev_8h.html for more information
DPDK (Data Plane Development Kit) subsystem mapping

## Slide 9: Leveraging OVS offloading capability with Marvell Octeon CN10K DPU

## Slide 10: Design Paradigm
Lower CPU Utilization
Free up CPU resources for other tasks, improving overall system efficiency
No Custom changes to OVS
Implement solutions without custom changes to OVS ensuring seamless integration of standard frameworks on Marvell platforms
Addressing Hardware Constraints
Mitigate hardware limitations through optimized software implementation that enhance overall functionality
Seamless Configuration
Utilize standard OVS utilities and network automation to simplify network configuration and management
OVS processes the initial packets and offloads the flow to hardware, enabling subsequent packets to be handled via fast path through hardware lookup
Optimizing Packet Processing
Maximize Hardware Utilization
Maximize hardware accelerators utilization by integrating with OVS hardware offloading features
© 2024 Marvell. All rights reserved.

## Slide 11: Navigating Packet Flow

## Slide 12
X86/ARM
Host
VM1
OVS
VF1-Rep
NIX + NPC
VFn-Rep
NIX-PF
Match | Action
Match1 | Action1
matchN | actionN
VMn
Match1 | Action1
Match2 | Action2
VMm
VFm-Rep
NIX + NPC
Flow Decoder
SDP VF1
SDP VFn
NIX VF1
NIX VFn
OVS-Offload-Engine
Encapsulation/Decapsulation Unit
OCTEON
Port
VM1 to VMn
Wire to VM1
First packet from wire is received by all VMs as result of ARP broadcast.
First packet from VM1 is steered to OVS for classification and flow offloading to the hardware.
Kernel VFm to Wire
VF port not part of ovs-offload application communicates with its respective OVS representor port HW via HW loopback block.
Tunnel Transfer
Subsequent packets hit the offloaded flow and reach VM1 directly.
Destined VM replies and gets the respective flow offloaded to hardware via OVS.
First packet from VMn undergoes encapsulation by OVS and same flow gets offloaded.
On reception OVS decapsulates the packet and steers the plain packet to VMn.
Match3 | Action2
Match4 | Action4
Wire to VM Exception path
VM to VM Exception Path
Tunneling exception path VM to wire
Native VF to Wire Exception path
Wire to VM Fast path
VM to VM Fast Path
Tunneling Fast path VM to wire
Native VF to Wire Fast path
© 2024 Marvell. All rights reserved.
Match1 | Action1
Match2 | Action2
Match3 | Action2
Match4 | Action4

## Slide 13: Feature Scaling with Modular DAO (Data Accelerator Offload) Components

## Slide 14
OCTEON
VM1
OVS
V1-Rep
NIX + NPC
PF
Match1 | Action1
Port
Hardware Offloading
Match | Action
Match1 | Action1
OVS-Offload-Engine
Flow Management
Flow Decoder
Encapsulation/Decapsulation Unit
MAC Learning
Ofproto/
Datpath Classifier
Flow Library
Flow/ Connection Aging
Connection Management
Flow Cascading
Flow Offloading to Hardware
Packet Transformation Library
Packet Tunneling (VxLAN, Geneve, GRE)
VLAN Tagging
Header Transformation​
NIX + NPC
X86/ARM Host
PCIe
Connection Tracking Library
Stateful/Stateless protocol tracking
Connection State Management
VM2
V2-Rep
Ethernet
Match | Action
Match1 | Action1
Match | Action
Match1 | Action1
Exception Path
Fast Path
Flow Management
Packet Manipulation
Packet Flow
Configuration Flow
Connection Management
Packet Classification
Match1 | Action1
DAO Components
© 2024 Marvell. All rights reserved.

## Slide 15
Certain protocols and actions not supported by the hardware
Optimized Software implementation for unsupported protocols and actions via DAO Flow library
Packets cannot be relayed directly from the host PCIe to Ethernet interface due to a lack of direct connectivity
OVS offload engine forwards packets between the host and Ethernet interfaces.
CN10K DPDK driver crashes when transmission is initiated from a non-pmd thread which carries an invalid lcore_id
Custom OVS change where a non-pmd thread registers for a valid lcore_id before transmission and deregister back on completion
No support for connection tracking offloads for DPDK provider
Enhancing OVS connection tracking for DPDK providers using rte_flow’s connection tracking capabilities
Challenges
Mitigations
Challenges
Small fraction of ARM cores is utilized to perform software tasks as part of the solution
Working on optimizing the ARM core utilization and offloading it to the hardware in future platforms

## Slide 16: Solution Milestones
Completed
Ongoing
Planned
Plain packet Switching Between Host VMs and outside network
Hardware offloading for VLAN tagged traffic
Tunnel Offloading with Optimized Software
Connection Tracking DAO Library
Advanced Flow management via DAO Flow library
  HW offloads enablement in OVS
Flow offloading and aging
    QoS
    IPsec
Cascaded flows
    Connection tracking offload for DPDK provider

## Slide 17: Summary
OVS HW offload feature improves system performance significantly
Synergizing Hardware and Software for Accelerated Packet Processing and Switching
Extra ARM cores available for business logic
Seamless integration with standard frameworks such as OpenShift, OVN
Feature Scaling with Modular DAO Libraries
Reusable solution for upcoming SoC